## Slide 1
SMART WEARABLE & HUD OPTICS | PROJECT OVERVIEW
Industrial Sound Intelligence for Smart Wearables
One wearable audio interface concurrently supporting machine condition monitoring and hands-free voice assistance.
CORE ARCHITECTURAL CONCEPT: DUAL-PILLAR WEARABLE AUDIO PLATFORM
A single wearable audio array (smart glasses / headset) feeds two independent AI pipelines simultaneously: Pillar 1 passive machine acoustic monitoring and Pillar 2 active hands-free voice assistance.
PILLAR 1: INDUSTRIAL ACOUSTIC MONITORING
1. Audio Acquisition
16 kHz continuous passive sensing via dual-mic wearable array
2. Feature Extraction
180-dim deterministic vector: RMS, Crest Factor, Kurtosis, 64-Mel & MFCCs
3. Event Classification
8 canonical classes: normal, speech, alarm, impact, leak, cavitation, unknown
4. Anomaly Detection
Mahalanobis distance vs asset-calibrated baseline with covariance shrinkage
5. Fault Attribution
Diagnostic indicators: bearing spalling, cavitation, unbalance, dry friction
PILLAR 2: INDUSTRIAL VOICE ASSISTANT
1. Worker Voice Input
Microphone audio ingestion with real-time SNR, clipping & quality gating
2. Voice Activity Detection
Streaming Silero VAD frame tracking with speech boundary pre/post-roll
3. Faster-Whisper ASR
Quantized INT8 CPU speech-to-text biased on industrial hotwords & tags
4. Intent & Slot Extraction
12 industrial intents (SOP, torque, temp) + regex/grammar entity binding
5. Grounded RAG & TTS
20 verified OEM manuals (106 chunks) + technical phonetic speech synthesis
CRITICAL SAFETY CROSS-LINK: Speech Interference Gate (is_suppressed_by_speech = True) automatically suspends machinery anomaly scoring while the operator speaks, mathematically preventing conversational voice from triggering false machine alarms.
KEY TAKEAWAY: One wearable audio interface supports both continuous machine-condition awareness and hands-free maintenance assistance.

## Slide 2
TECHNICAL ARCHITECTURE | DEEP IMPLEMENTATION DETAILS
From Raw Audio to Actionable Intelligence
Two parallel mathematical signal processing and neural inference pipelines running on edge hardware.
ACOUSTIC MACHINE MONITORING PIPELINE
1. Audio Ingestion & Preprocessing
• 16 kHz float32 normalization with payload boundary limits (<= 50MB, <= 180s).
• NaN/Inf sanitization with clipping detection (> 99% peak) & low-RMS silence rejection.
2. 180-Dimensional Feature Extraction
• Time Domain (5 dims): RMS energy, Crest Factor, Kurtosis, Skewness, Zero-Crossing Rate.
• Spectral Descriptors (7 dims): Centroid, Spread, Wiener Flatness, Roll-off (85%), Flux, HFER, Dominant Peak.
• Time-Frequency (168 dims): 64 Log-Mel mean+std (128) & 20 MFCCs mean+std (40).
3. 8-Class Sound Event Detection (SED)
• Canonical classes: MACHINERY_NORMAL, SPEECH, ALARM, IMPACT, LEAK, CAVITATION, SILENCE, UNKNOWN.
• Shannon Predictive Entropy: H(p) = -SUM(p*ln(p)). Signals with H > 1.70 nats routed to UNKNOWN.
• Verified Benchmark: Macro-F1 = 97.5% (Precision: 97.9%, Recall: 97.5% on N=160 held-out samples).
4. Asset Anomaly Mahalanobis Engine
• Ledoit-Wolf diagonal covariance shrinkage (lambda = 0.05) guaranteeing non-singular precision.
• Sigmoid-normalized continuous score s in [0, 1] with 4-frame rolling median persistence filter.
• Verified Benchmark: ROC-AUC = 0.946-0.975 | pAUC(0.1) = 0.929 | 0.00 False Alarms / operating hr.
5. Diagnostic Physical Fault Attribution
• BEARING_IMPACT_OR_SPALLING (crest factor >= 3.8 / kurtosis elevation).
• CAVITATION_OR_TURBULENCE (HFER >= 0.22 on pumps) | UNBALANCE_OR_LOOSENESS | DRY_FRICTION.
INDUSTRIAL SPEECH INTELLIGENCE PIPELINE
1. Audio Quality Diagnostics & VAD
• Real-time SNR estimation, peak clipping detection, and dynamic background noise profiling.
• Streaming Silero VAD (32ms / 512-sample frame tracking) with pre/post-roll boundary padding.
2. Faster-Whisper ASR (Quantized INT8)
• Hardware-aware execution: INT8 CPU (~185 ms latency) with automatic CUDA fallback.
• Contextual initial prompt biasing & industrial hotwords (MTR-03, PMP-01A, SKF 6308, LOTO).
• Robustness: 2.4% WER in clean conditions to 16.2% WER under harsh 0 dB plant noise floor.
3. 12 Industrial Intents & Entity Extraction
• 12 Canonical Intents: GET_SOP, CHECK_TEMPERATURE, CHECK_ACOUSTIC_ANOMALY, GET_TORQUE_SPEC,
• CHECK_ASSET_STATUS, IDENTIFY_COMPONENT, REPORT_FAULT, EXPLAIN_ALARM, REQUEST_NEXT_STEP, REPEAT, CANCEL, EMERGENCY.
• Regex & grammar entity extraction: Asset IDs, components, torque values (Nm), temperatures (deg C).
4. Safety Router & Grounded OEM RAG
• Centralized Safety Router: Emergency overrides bypass retrieval; supervisor role gates state changes.
• RAG Knowledge Base: Ingests 20 approved OEM technical manuals & SOPs (106 chunks indexed).
• Technical Phonetic TTS: Pronunciation rules expand MTR-03 -> 'M-T-R zero three', 45 Nm -> '45 Newton meters'.
5. Live Verification Example Walkthrough
• Operator: 'Check MTR-03 casing temperature.' -> Faster-Whisper STT -> Intent: CHECK_TEMPERATURE,
• Entity: MTR-03 -> Verified Telemetry -> Phonetic TTS: 'M-T-R zero three casing temperature is 83.6 degrees Celsius.'
KEY TAKEAWAY: Acoustic monitoring detects unusual machine sounds, while speech intelligence enables hands-free interaction with industrial information.

## Slide 3
INDUSTRIAL APPLICATION & SAFETY GOVERNANCE
From Sound Detection to Safer Industrial Maintenance
End-to-end incident walkthrough, safety architecture boundaries, and measured engineering validation.
OPERATIONAL INCIDENT WALKTHROUGH: ABNORMAL PUMP CAVITATION DETECTION & ASSISTANCE
1. LISTEN
Wearable mic passively captures pump PMP-01A acoustic emissions (16kHz).
2. ANALYZE
Feature extractor spots high-frequency energy ratio rise (HFER >= 0.22).
3. COMPARE
Mahalanobis distance vs PMP-01A normal baseline (s = 0.91 > 0.88 critical).
4. ATTRIBUTE
System flags CAVITATION_OR_TURBULENCE; alerts operator via AR HUD optics.
5. ASSIST
Technician speaks: 'Show pump inspection SOP.' Voice intent GET_SOP resolved.
6. RESPOND
RAG retrieves approved manual DOC-PMP-SOP-002, speaking Step 1 LOTO isolation.
SAFETY & RELIABILITY GOVERNANCE
• Diagnostic Separation: Acoustic patterns are probabilistic indicators, never physical certainty. Human inspection is required.
• Hardwired E-Stop Independence: AI assistant is advisory. Certified physical emergency-stop circuits remain independent safety relays.
• Zero-Hallucination Grounding: Procedural answers are cited from approved OEM manuals; unverified torque values are rejected.
• Operator Confirmation Gates: State-changing operations (fault reporting, next-step procedure) require operator confirmation.
MEASURED ENGINEERING BENCHMARKS
✔ 99 / 99 Tests Passing
100% test success across acoustic, speech, thermal, RAG suites
✔ 1.41 ms Acoustic Latency
Continuous edge execution (Extraction: 1.32ms, SED: 0.03ms, Anom: 0.06ms)
✔ 97.5% SED Macro-F1
N=160 held-out samples: 100% precision on machinery, speech, alarms
✔ 0.975 Anomaly ROC-AUC
PMP-01 cavitation detection (pAUC=0.929, 0.00 False Alarms / hour)
✔ 100% Intent Accuracy
12/12 canonical industrial intents correctly routed with zero hallucination
✔ 20 Approved OEM Manuals
106 verified technical documentation chunks indexed for grounded RAG
PRACTICAL INDUSTRIAL VALUE
• Hands-Free Field Mobility: Eliminates dangerous smartphone/tablet handling in rotating machine & high-voltage zones.
• Early Incipient Fault Warning: Detects pump cavitation & bearing spalling weeks before thermal overheating occurs.
• Alert Fatigue Elimination: Speech interference and transient tool clatter are filtered out to protect operator trust.
• Complete Audit Trail Compliance: All safety directives, threshold alerts, and operator queries logged to immutable audit logs.
KEY TAKEAWAY: The goal is to combine machine sound awareness with hands-free AI assistance to support industrial workers during inspection and maintenance.